## Slide 1: Cerenkov Counters Threshold Ring Imaging (RICH) Direct Internal Reflection (DIRC)
Charles Hyde
18 July 2011
Old Dominion University

## Slide 2: Cerenkov Radiation
Four-vector current of a point charge q travelling at velocity v through a medium of index of refraction n
  Jµ = [rc, J] = q vm d(3)(r-vt) vm = [c, v]
Maxwell’s equation for the vector potential in medium
  ☐nAµ = 4p Jµ
  Fourier transform and invert with Cauchy integral
Classical or Quantal solution
  Light is emitted in a broadband pulse with wave-vectors pointing in a cone of half angle given by cosqC = 1/(n v/c)
  Optical analog of sonic boom for all wavelengths l of light s.t. n(l) > v/c

## Slide 3: Cerenkov Cone
Constant phase
  l = vacuum wavelength.
  f = c/l = optical frequency
  cosqC= c/(nv)
    qC 0 as vc/n+
v>c/n(l)
l/n(l)
v/f
qC
l/n(l)
v/f = lv/c
qC

## Slide 4: Cerenkov Light Intensity
pdg.lbl.gov: Chapter 23.7, or solve for Aµ
  Number of photons produced per unit particle pathlength dx (charge ze and speed v) and per unit wavelength bandwidth dl in medium of index of refraction n(l).
Example: high energy electron (v/c≈1) in CO2 at STP.
  n=1.0000+4.1•10-4
  Integrate l from 300 to 600 nm (typical PMT sensitivity)
    dN/dx ≈ 30 optical photons per meter of flight path
    Multiply by 20% Quantum Efficiency of PMT
      6 photo-electrons detected per meter of flight path in active gas.
      One photo-electron is one electron knocked out off the photocathode by a photon. Typical PMT gain is 106 with pulse in 10 ns = 160µA pulse per photo-electron = 8 mV into 50W.
Increase signal by extending PMT sensitivity into UV.
  50% gain if cutoff extended to 200 nm
  UV optics, UV transparent PMT glass are expensive
  n1 as l  X-ray, natural cutoff of Cerenkov emission.
RF Cerenkov emission exists, but is too weak (1/l2) for single particle detection.

## Slide 5: Cerenkov Detector as Particle Identifier
Cerenkov Detectors are sensitive to particle velocity.
Tracking in magnetic field determines particle momentum.
p = mvg
Cerenkov + Tracking  Mass  ID
Particle ID is hard
  Worth the effort to get every Cerenkov photo-electron

## Slide 6: Threshold Cerenkov Detector Hall A High Resolution Spectrometer
HRS Detector Stack
1.0-1.5 m CO2 Cerenkov
  1 atm
  60x220 cm2 aperture for incident particles
  Ten mirrors, directing light to ten 5”f PMT
  ≈ 7 photo-electrons (p.e.)

## Slide 7: Electron I.D. in CO2 Cerenkov
Threshold for light emission v/c > 1/n p > mc/[(n+1)(n-1)]1/2 n-1 = 4.1•10-4
  Electron threshold (mec2= 511KeV):
    pe > 18 MeV/c
    As vec, qC1.6°
  Charged pion threshold (mc2=140 MeV):
    pp> 4.8 GeV/c
For momenta from 0.02 to 4.8 GeV/c, if a particle makes a Cerenkov signal in the CO2, than it is an electron.
  Particle ID is not 100% robust.
    For pπ > 0.6 GeV/c, the pion can kick out an energetic electron (d-ray) with pe> 20 MeV/c. This electron can produce a full Cerenkov signal and give a false electron i.d. This happens with 1-2% probability.
  Supplement Electron I.D. with an Electromagnetic Shower Counter / Calorimeter.

## Slide 8: Pion/Kaon I.D. in a threshold Cerenkov Detector
Aerogel detector.
  Aerogel is a SiO2–air colloid. The granularity is smaller than the wavelength of light. Approximately homogenous, extremely light material (a little bit visibly cloudy, and extremely hydroscopic).
  Material Parameters:
    density r = 0.1—0.3 g/cm3,
    n-1.0 = 0.25r = 1.025 – 1.075
    Bridges gap from gasses (n-1 <0.001) to liquids and solids (n>1.2)
Hall A Threshold Aerogel Cerenkov
  n=1.025
    Threshold for charged pions: pπ > 0.63 GeV/c
    Threshold for charged kaons (mKc2 = 0.5 GeV): pK > 2.2 GeV/c
  A particle of momentum between 0.6 and 2.2 GeV/c that fails to fire the Aerogel Cerenkov must be heavier than a pion
    Candidate kaon or proton.
    Use time of flight (direct measure of speed for protons with p < 2 GeV/c

## Slide 9: Ring Imaging Cerenkov Counter
Two particles of equal momentum, but different masses, will produce Cerenkov light cones of different opening angles q1, q2.
An optical system of focal length f will image the Cerenkov cones onto circles of radius f tanqC.
Measure ri=f tanqi
  qi= tan-1(ri/f)

## Slide 10: HERMES Experimental Setup
e+N  e’ + h +X in DIS
2 identical RICH modules

## Slide 11: HERMES Dual Radiator RICH Nuclear Instruments and Methods in Physics Research A 479 (2002) 511–530
Aerogel and C4F10.
  425 Aerogel tiles per module
8 Mirrors per module
2000 Philips XP1911 (¾”) PMTs per module
Two modules (above and below 27 GeV electron beam)

## Slide 12: Hadron PID: HERMES RICH: NIMA 479 (2002) 511-530
Two radiators: aerogel and gas
PMTs as photon detector
Focusing Optics
resolution dq ≈ 10 mr
5.5 GeV K+
14.6 GeV e-
1.5 GeV p-
REAL DATA from NIMA 479 (2002) 511
C4F10 gas
Identify p, K and p
from 2 to >12 GeV/c
aerogel
gas
(e,e’p-K+)X event

## Slide 13: HERMES Dual RICH performance
2x2000 PMT
For a b≈1 particle
  Aerogel ring ≈ 10p.e.
  C4F10 ring ≈ 20 p.e.
Angular resolution: dqC ≈ ±10 mr
5.5 GeV/c kaon, Aerogel ring, no gas ring.
1.5 GeV/c π-, Aerogel ring, no gas ring.
14.6 GeV/c e-, Aerogel ring and gas ring.
Slower particles give bigger rings, until at v=c/n, qC90° & r∞

## Slide 14: CLAS12 Dual RICH
Small angle, photo-sensors must be “inside”.
C4F10
Mirror
Aerogel
PMTs

## Slide 15: Conceptual Layout for an Electron-ion Collider at JLab (2020s)
Three compact rings:
3 to 11 GeV electron
Up to 12 GeV/c proton (warm)
Up to 90 GeV/c proton (cold)
Upgrade option to ~ 200 GeV/c proton

## Slide 16: EIC Detector Cartoons

## Slide 17: BABAR layout
Instrumented Flux Return
19 layers of RPCs, (upgraded to LSTs)
1.5 T Solenoid
DIRC
Drift Chamber
40 layers (24 stereo)
Electromagnetic Calorimeter
6 580 CsI crystals
Silicon Vertex Detector
5 layers of double sided silicon strips
e– (9.0 GeV)
e+ (3.1 GeV)
center of mass energy  M(4S) =10.58 GeV/c2
bg = 0.56
THE BABAR DETECTOR
All BABAR DIRC slides today: J.S., RICH 2002/4, Giessen 2009

## Slide 18
DIRC thickness:
2 cm SiO2 active
8 cm radial incl. supports
19% radiation length
at normal incidence
DIRC radiators cover: 94% azimuth,
83% c.m. polar angle
DIRC photon detection array:
10,752 PMTs ETL 9125
THE DIRC IN BABAR

## Slide 19: Total Internal Reflection of Cerenkov Light
Fused Silica
  n(SiO2) = 1.47
  Industrial production processes
  Highly transparent from 180 to 800 nm
Cerenkov angle qC = 47°
  qC(pion at 2 GeV/c) = 47.0°
  qC(kaon at 2 GeV/c) = 45.5°
    DqC(2 GeV/c) = 27 mr
    DqC(4 GeV/c) = 7 mr
cosqC < sinqC  total internal reflection at normal track incidence.

## Slide 20
Bar box: 12 bar boxes in BABAR
12 long (4.9m) bars per box
17.25 mm thick ×35 mm wide
150μm air gap between bars
dry nitrogen flow
Long bar: 4 short (1.225m) bars
Fused silica (SiO2)
Mirror on forward end
Wedge on readout end
THE DIRC IN BABAR
H2O
11000
PMTs
(29mmf)

## Slide 21: BABAR DIRC Pinhole Proximity Imaging
Non focusing image formation in expansion volume of 6000 litre pure H2O
Roughly 1m radius volume
Simple analysis: Ignore
  n(SiO2)-n(H20)= 1.47-1.33 difference.
  6 mr incline of bottom of wedge
Consider two particles of different velocities passing through the 17 mm thickness
  The two tracks produce two wedges of parallel light at angles q1 and q2 in the plane of a particular azimuth of the Cerenkov cone.
  The light from each track illuminates 17 mm in vertical ascension, or ~ 1 PMT
  The images of these two light sources will be separated by L(q2- q1) ≈ (1 m) Dq
  Single pixel resolution by L(q2- q1) > 29 mm/√12 = one-s spatial resolution of single PMT (diameter 29 mm).
  Angular resolution dq ≈ [(29 mm)/(1.0 m)] / √(12 Npe)
    Npe = Number of photo electrons detected > 25
    dq ≈ 1.5 mr (rms)
6 mr incline at bottom of wedge
  Half of light has last reflection off bottom of bar: q = qC
  Half of light has last reflection off bottom of wedge: q = qCv+ 6 mr.
  Vertical image size is reduced by (1m)(6mr) to ~ 12 mm.

## Slide 22
 300 nsec trigger window   8 nsec Dt window (~500-1300 background hits/event) (1-2 background hits/sector/event)
Calculate expected arrival time of Cherenkov photon based on • track TOF • photon propagation in radiator bar and in water
Dt: difference between measured and expected arrival time

s(Dt) = 1.7 nsec
Dt (nsec)
For BABAR DIRC time information provided powerful tool to reject accelerator and event related background.
Dt also used to determine event time for “self-triggering” of DIRC.
DIRC RECONSTRUCTION
Notes: 22

## Slide 23
Example: Comparison of real event to simulated response of BABAR DIRC to e/p/K/p.
DIRC likelihood Calculate unbiased likelihood for observed PMT signals to originate from e///K/p track or from background. ( Likelihood: Pdf(qc)  Pdf(Dt)  Pdf(Ng) ) Two complementary reconstruction algorithms: • iterative process to maximize event likelihood, full correlation of all tracks; • individual track fit provides qc, s(qc), number of signal/background photons. Reflection ambiguities: for BABAR Dt cut reduced these from up to 16 to typically 2-3
Particle ID is based on log likelihood differences of the five hypotheses.
DIRC RECONSTRUCTION
Notes: 23

## Slide 24: DIRC Resolution

## Slide 25: Chromaticity
Chart: Fused Silica
| 180.0 | 190.0 | 200.0 | 213.9 | 226.7 | 230.2 | 239.9 | 248.3 | 265.2 | 275.3 | 280.3 | 289.4 | 296.7 | 302.2 | 330.3 | 340.4 | 351.1 | 361.1 | 365.0 | 404.7 | 435.8 | 441.6 | 457.9 | 476.5 | 486.1 | 488.0 | 496.5 | 514.5 | 532.0 | 546.1 | 587.6 | 589.3 | 632.8 | 643.8 | 656.3 | 694.3 | 706.5 | 786.0 | 820.0 | 830.0 | 852.1 | 904.0 | 1014.0 | 1064.0 | 1100.0 | 1200.0 | 1300.0 | 1400.0 | 1500.0 | 1550.0 | 1660.0 | 1700.0 | 1800.0 | 1900.0 | 2000.0 | 2100.0
Index of Refraction | 1.5853 | 1.5657 | 1.5505 | 1.5343 | 1.5228 | 1.5201 | 1.5134 | 1.5084 | 1.5 | 1.4959 | 1.494 | 1.491 | 1.4887 | 1.4872 | 1.4805 | 1.4786 | 1.4767 | 1.4751 | 1.4745 | 1.4696 | 1.4667 | 1.4662 | 1.465 | 1.4637 | 1.4631 | 1.463 | 1.4625 | 1.4616 | 1.4607 | 1.4601 | 1.4585 | 1.4584 | 1.457 | 1.4567 | 1.4564 | 1.4554 | 1.4551 | 1.4536 | 1.453 | 1.4528 | 1.4525 | 1.4517 | 1.4502 | 1.4496 | 1.4492 | 1.4481 | 1.4469 | 1.4458 | 1.4446 | 1.444 | 1.4427 | 1.4422 | 1.4409 | 1.4395 | 1.4381 | 1.4366
ThetaC | 0.88821 | 0.87801 | 0.86984 | 0.8609 | 0.85435 | 0.85282 | 0.84894 | 0.84604 | 0.84109 | 0.83862 | 0.83749 | 0.83565 | 0.83428 | 0.83334 | 0.82925 | 0.82803 | 0.82687 | 0.82589 | 0.82552 | 0.82242 | 0.82057 | 0.82027 | 0.81948 | 0.81867 | 0.8183 | 0.81822 | 0.81791 | 0.81729 | 0.81674 | 0.81634 | 0.81529 | 0.81525 | 0.81436 | 0.81415 | 0.81394 | 0.81332 | 0.81315 | 0.81211 | 0.81174 | 0.81163 | 0.8114 | 0.8109 | 0.80994 | 0.80954 | 0.80926 | 0.8085 | 0.80775 | 0.807 | 0.80623 | 0.80583 | 0.80493 | 0.8046 | 0.80373 | 0.80282 | 0.80187 | 0.80086

## Slide 26: Topics for EIC R&D
Conventional design
  SiO2 penetrating Flux return on electron side
  Expansion volume and ≥ 10,000 PMT
Compact Design inside magnetic field
  Focusing optics (prism, mirrors), expected readout 30x30 cm2
  Small pixel size photo-detectors
    Micro Channel Plate PMT
    SiPMT
  Test performance in magnetic field up to 4 Tesla
Simulate Cerenkov Reconstruction
Simulate backgrounds
  Beam related neutrons
  Synchrotron Radiation X-rays
  Bremsstrahlung, etc.

## Slide 27: Compact Photo-Sensors
Metal channel PMT
(3mm)2 pixel size
Q.E. 20%
  Improvements to 40%?

## Slide 28: µChannelPlate (MCP)
typical channel diameter 6-10 µm
  R&D for 2µm
  pixel size limited by channel diameter.
Two MCP stages in chevron pattern to achieve gain ~106
Budker Institute (Novosibirsk) for PANDA DIRC
Very fast!
  30 ps TTS (1 p.e.)
Q.E. ~ 20%
packing fraction ~25%
  use lenses to focus onto active area?
Moderate sensitivity to high magnetic fields
http://hea-www.harvard.edu/HRC/mcp/fmcp.gif
Barnyakov, NIMA567 (2006)
instr08.inp.nsk.su/reports/Barnyakov.pdf
Burle, 5 micron and 2 micron

## Slide 29: MCP-PMT in 1-2 Tesla Magnetic Field
Budker Institute
  Gain decrease by factor 0.2 in 1.6 T field at 30°
  Quantum Efficiency decreases by only 20%

## Slide 30: Photo-sensors
MultiPixelPhotonCounter (MPPC) = SiPMT
Geiger avalanche saturates each pixel
  Each pixel is saturated by a single photo-electron
  Pixels can be ganged together for multi-photon detection at lower granularity.
  900 pixels (100µ)2 in 3mm x 3mm format
  Gain ~106
  time resolution 500 ps rms per photon
  Fill factor up to 80%
  Quantum Efficiency up to 65%
  Noise: 10 KHz/pixel at 0.5 p.e. threshold
  Operating bias voltage ~70 V
Rapid development
  60,000 MPPC for T2K Near Detector
© Hamamatsu

## Slide 31
p
PANDA DETECTOR
Barrel DIRC
Endcap DIRC
EM Calorimeter (lead tungstate)

## Slide 32
Particle Identification coverage of the two DIRC detectors
Kaon distribution of the radiative decay J/ψ -> K+K- γ
(search of glue balls)
Endcap
Barrel DIRC
Endcap Disk DIRC
Disk DIRC
Barrel DIRC
DIRC IN PANDA

## Slide 33: PANDA BARREL DIRC
Improved version of proven BABAR-DIRC design
More compact, faster, focusing optics
  96 radiator bars, synthetic fused silica 17mm (T) × 33mm (W) × 2500mm (L)
  Focusing optics: lens system
  Compact photon detector: array of Burle Planacon MCP-PMT or Geiger-mode APD, total 7000-10000 channels.
  Fast photon detection: MCP-PMT/gAPD plus fast TDC/ADC (ToT) electronics → 100-200 ps timing.
Still investigating several design options:
mirror focusing, radiator plates, photon detection outside magnetic field
Radiator bars
Photon detectors and electronics
Focusing optics

## Slide 34
FDIRC FOR ITALIAN SUPERB
Focusing DIRC (FDIRC) Design: large synthetic fused silica block (Corning) for expansion region and focusing.
“Camera” approach: each of the 12 bar boxes read out with one optically isolated block/readout module.
Additional wedge required to image all photons on cylindrical mirror of focusing block.
side view
G4 model
Figures from J. Va’vra RICH2010

## Slide 35
Image reconstruction in 2D (X, Y)
Timing used for event correlation and background subtraction
Radiator: synthetic fused silica, 20 mm thick, 1100 mm radius
Focusing optics for imaging with dispersion correcting element (LiF)
Compact detection plane on each light guide (50x50 mm2)
128 light guides, 4096 R/O channels
PANDA FOCUSING DISK DIRC
fused silica disk
lightguides and photon detectors
mechanical support
Notes: explain radiator choice
explain mechanical constraints

## Slide 36
Direct measurement of Cherenkov angle → need expansion region
Design of expansion region = light guide compromise between compact size and performance with given MCP-PMT size
Transition from fused silica to LiF and back has two-fold prism effect and mitigates dispersion
PANDA FOCUSING DISK DIRC

## Slide 37: Limitations on DIRC Resolution
Pixel size
  (adjustable by focusing optics, expansion volume, Photo Sensor technology)
Tracking Resolution
  Need ~ 1mr prediction of axis of Cerenkov cone
Flatness and Parallelism of Fused-Silica
  Industrial process ~ $10K/bar

## Slide 38: BNL funded EIC Detector R&D grant
How can we best adapt and improve the DIRC concept for an EIC detector.
  Simulations and design work
  Prototyping with GSI
  Photosensor testing at JLab?
Three year proposal.
  $115K funded in first year to ODU, JLab, CUA, GSI collaboration.
  Second and Third year funding to be resubmitted in Nov. 2011.

## Slide 39
PANDA BARREL DIRC DESIGN
Barrel DIRC design, readout inside magnet yoke. (prelim. dimensions)
Barrel radius ~50 cm, length ~250 cm, gap (2*one bar) for target pipe at 12 o’clock and 6 o’clock,
Expansion volume depth ~30 cm, height ~50cm (plus space for PMTs and cables).

## Slide 40: HERMES single event display
(e,e’)X event.

## Slide 41: Ring Imaging Cerenkov Counter: PID
Two particles of equal momentum, but different masses,
  Cerenkov light cones of opening angles q1, q2.
  Focused rings of radii ri = f tanqi