## Slide 1: Transportation Research Board (TRB) Conference
Unloading and Pre-Marshalling Algorithms with Java Computer Animation for Terminal Yard Operations January 10-14, 2016
Ivan Makohon
Graduate Student*
Modeling, Simulation & Visualization Engineering (MSVE) Department
Phone: 757-481-0832
imako001@odu.edu
Mecit Cetin (corresponding author)
Associate Professor*
Civil & Environmental Engineering (CEE) Department
Phone: 757-683-6700
mcetin@odu.edu
Duc T. Nguyen
Professor*
CEE and MSVE Departments
Phone: 757-683-3761
dnguyen@odu.edu
*Old Dominion University
Manwo Ng
Assistant Professor*
Department of Information Technology and Decision Sciences
Phone: 757-683-6665
mng@odu.edu

## Slide 2: Abstract
Unloading and pre-marshalling (or reshuffling) operations have been considered as basic/important tasks in port terminals’ activities, since the economic impacts can be significant. The primary goal for this paper is to develop simple heuristic unloading and pre-marshalling algorithms. Detailed explanations for the proposed algorithms are given in the form of step-by-step numerical procedures, so that the reported results can be reproduced by the readers. Several numerical examples (including the ones considered by other researchers) are used to validate the proposed unloading and pre-marshalling algorithms.
A secondary goal for this paper is to develop a user-friendly and easy-to-use Java Graphical User Interface (GUI) software application that provides precise and clear step-by-step instructions with visual animation and voice for the unloading and pre-marshalling algorithms for Terminal Container Yard operations. The developed Java software can be used as an additional/educational tool that would serve both academia students and transportation professionals in solving any complex dynamic Terminal Container Yard layout visually with provided steps to show the “final/optimal” results. A demo video of the both the unloading and pre-marshalling algorithm’s animation and result can be viewed online from any web browser using the website provided in reference [4].
Keywords: Terminal, Yard, Cargo, Container, Unloading, Pre-marshalling, Reshuffling, Algorithm, Java, Animation

## Slide 3: Overview (1 of 2)
Container Terminal Yard Operations:
  Quay Crane (Port-side) unload cargo containers from docked vessels pier side to horizontal transport trucks which transports them to the container yards.
  Container Yards are storage yards for cargo containers.
  Container trucks transport cargo containers to their destinations.
Yard Crane
Container Yard
Quay Crane (Port Side)
Vessel
Transport
(Horizontal)
Container Truck

## Slide 4: Overview (1 of 2)
Container Terminal Yard:
  Crane The yard crane that services bays.
  Bay Contains a set of container stacks.
  Stack Contains stackable cargo containers up to MNCPS.
  Tier Height (level) of the stack.
Legend
Bay
Stack
Tier
Yard Crane
Container Yard

## Slide 5: Introduction
Container Terminal Yards are an import storage point since it links the seaside with landside transportation. It’s an important storage point for loading/unloading cargo containers between vessels and vehicles (i.e. trucks or trains) for further distribution.
Increasing traffic of cargo container shipments around the world which is why critical planning decision with great importance is needed for optimizing the terminal container yard’s unloading and pre-marshalling (or reshuffling) for cargo containers within the container yard.
Very similar to the Blocks World planning domain problem which consists of a finite number of blocks stacked into columns. The goal is to turn the initial state into a goal state with the minimal number of moves. This would save time in port operations which would lead to significant economic gains.
Two algorithms (unloading and pre-marshalling) are revisited with the primary goal to demonstrate simple heuristic algorithm for port operations to visually showing step-by-step animation to solve for the unloading and pre-marshalling problem.

## Slide 6: Unloading Algorithm
The Unloading Algorithm approach is based upon having the container stacks reshuffled to get to the priority cargo container when a vehicle arrives.
  When a vehicle arrives for pick up, the container stack is then reshuffled to get to the priority cargo container so that it can be unloaded onto the vehicle.
  The container stacks remain the same until the next vehicle arrives.

## Slide 7: Unloading Algorithm (1 of 5)
8
1
7
5
2
4
6
3
7
5
2
4
6
3
8
1
1
8
  Move 8 to Stack 2
  Unload 1
  NM = 1, NR = 1
  Initial Layout
  NS = 4, MNCPS = 3
  NS > MNCPS
  NM = 0, NR = 0

## Slide 8: Unloading Algorithm (2 of 5)
7
5
4
8
6
3
3
6
7
6
3
4
2
8
5
2
4
  Move 4 to Stack 1
  Unload 2
  NM = 2, NR = 2
  Move 6 to Stack 2
  Unload 3
  NM = 3, NR = 3

## Slide 9: Unloading Algorithm (3 of 5)
7
6
8
5
5
7
6
4
8
5
  Unload 4
  NM = 3, NR = 4
  Unload 5
  NM = 3, NR = 5
5
4

## Slide 10: Unloading Algorithm (4 of 5)
8
7
7
6
6
  Unload 6
  NM = 3, NR = 6
  Move 8 to Stack 1
  Unload 7
  NM = 4, NR = 7
8
7
8

## Slide 11: Unloading Algorithm (5 of 5)
8
8
  Unload 8
  NM = 4, NR = 8
  Done Unloading
  NM = 4, NR = 8

## Slide 12: Unloading Algorithm (1 of 4)
Layout Validation: Determine if there’s enough empty spaces to perform the algorithm.
  If the number of available empty spaces (NAES) is greater-than or equal to the number of empty spaces required (NESR) minus 1. The NESR-1 should allow us to get to the priority cargo container for removal.
  If the number of container stack (NS) is greater-than 1 container stacks. Need at least 2 or more container stacks to be able to do unloading. NAES should provide enough empty spaces initially to get to the priority cargo container if it’s on the bottom.

## Slide 13: Unloading Algorithm (2 of 4)
Step 0: Initialization
  Initialize the Number of Stacks (NS)
  Initialize the Maximum Number of Containers Per Stack (MNCPS)
  Initialize the initial stack layout
  Initialized variable for determining the number of spaces available
Step 1: Verify the Number of available spaces required (do only once)
  Simple check to determine if number available spaces is greater-than equal to the number of number of empty spaces required (in our case we use MNCPS)

## Slide 14: Unloading Algorithm (3 of 4)
Step 2: Find next cargo container to be removed
Step 2.1: Determine if cargo container is on top of the stack
  If stacks are empty
    We are done.
  Else if next cargo container to be removed is on top
    Proceed to Step 4: Remove Container
  Else if next cargo container not on top
    Proceed to Step 3: Move Container
  Proceed to Step 2: Find next cargo container to be removed

## Slide 15: Unloading Algorithm (4 of 4)
Step 3: Move Container
  Determine the stack with the highest-lowest cargo container
  Move cargo container to that stack
Step 4: Remove Container
  Remove (pop) the cargo container from the stack

## Slide 16: Pre-Marshalling (Reshuffling) Algorithm
The pre-marshalling (reshuffling) algorithm approach is based on having the container stacks ordered before the first vehicle arrives so that the priority container is on top.
  No more reshuffling is required since the container stacks are reshuffled with the priority containers on top prior to the first vehicle arriving.
  As each vehicle arrives, the priority container is on top and is unloading onto the vehicle.

## Slide 17: Pre-Marshalling Algorithm (1 of 3)
8
1
7
5
2
4
6
3
7
5
2
4
3
  Move 6 to Stack 2
  NM = 1, NR = 0
  Initial Layout
  NS = 4; MNCPS = 3
  NS > MNCPS
  NM = 0, NR = 0
8
1
6
6

## Slide 18: Pre-Marshalling Algorithm (2 of 3)
5
2
4
  Move 8 to Stack 4
  NM = 3, NR = 0
  Move 3 to Stack 2
  NM = 2, NR = 0
3
1
7
6
8
8
5
2
4
8
1
7
6
3
3

## Slide 19: Pre-Marshalling Algorithm (3 of 3)
1
7
6
3
4
8
  Done Reshuffling
  Begin Unloading
  NM = 4, NR = 0  8
  Move 4 to Stack 4
  NM = 4, NR = 0
5
3
1
7
6
4
2
8
4
5
2

## Slide 20: Pre-Marshalling Algorithm (1 of 4)
Layout Validation: Determine if there’s enough empty spaces to perform the algorithm.
  If the number of available empty spaces (NAES) is greater-than or equal to the number of empty spaces required (NESR). Need NAES in order to do reshuffling without removal.
  If the number of container stacks (NS) is greater-than 2 container stacks. Need at least 3 or more container stacks to be able to do reshuffling. Note: some layouts can be solved without these validations for reshuffling, though these verifications avoid deadlock cases.

## Slide 21: Pre-Marshalling Algorithm (2 of 4)
Step 0: Initialization
  Initialize the Number of Stacks (NS)
  Initialize the Maximum Number of Containers Per Stack (MNCPS)
  Initialize the initial stack layout
  Initialized variable for determining the number of spaces available
Step 1: Verify the Number of available spaces required (do only once)
  Simple check to determine if number available spaces is greater-than equal to the number of number of empty spaces required (in our case we use MNCPS)

## Slide 22: Pre-Marshalling Algorithm (3 of 4)
Step 2: Reshuffle Stacks
  Determine if all the stacks are in order, if so proceed to Step 4: Removing Containers From Stacks.
  Calculate costs for all stacks (determine the number of moves)
  Find container with the lowest cost value (number of moves).
  If cost value is greater-than 0.0
    Perform Step 2.1
  Else if cost is equal-to 0.0
    Perform Step 3: Move Containers (info is provided from Calculating Costs for all stacks)
  Perform Step 2: Reshuffle Stacks (Recursion)
Step 2.1: Determine if there’s a Stack with One container that can be moved
  If so then try to find a stack that’s in order with a container with the highest-lowest container that this container being moved. Also, check stack to determine if it’s less-than MNCPS.

## Slide 23: Pre-Marshalling Algorithm (4 of 4)
Step 3: Move Container
  Move cargo container to container stack. Basically, removes (pops) the cargo container from the existing (source) stack and adds (pushes) it to the new (destination) stack.
Step 4: Removing Containers From Stacks
  Stack should be in order (lowest (on top) and highest (on bottom)).
  Loop through container stack and find the next lowest cargo container to be removed.

## Slide 24: Java Computer Animation (1 of 3)
A user-friendly and easy-to-use Java Graphical User Interface (GUI) software application that provides precise and clear step-by-step instructions with visual animation and voice for the unloading and pre-marshalling algorithms for Terminal Container Yard operations.
The software can be used as an additional/educational tool that would serve both academia students and transportation professionals in solving any complex dynamic Terminal Container Yard layout visually with provided steps to show the “final/optimal” results.

## Slide 25: Java Computer Animation (2 of 3)
MAIN Graphical User Interface (GUI):
Menu Buttons (File, Preferences, and Help)
Input Control Buttons
Terminal Yard Layout (Animation View)
Status View
Lesson Control Buttons
Algorithm Step
Tutorial Information View
Terminal Yard Layout (Initial View)

## Slide 26: Java Computer Animation (3 of 3)
Terminal Yard Editor GUI:
Display & Information View
Editor Buttons
Zoom Buttons
Visualization Editor View
Confirmation/Close Button

## Slide 27: Unloading Algorithm Demo

## Slide 28: Pre-Marshalling Algorithm Demo

## Slide 29: Terminal Yard Editor Demo

## Slide 30: Experimental Results

## Slide 31: Questions/Comments

## Slide 32: Acronyms
NS Number of Stacks
MNCPS Maximum Number of Containers Per Stack
NAES Number of Available Empty Spaces (a.k.a. NAES = TNS – NCC)
NESR Number of Empty Spaces Required (a.k.a. NESR = MNCPS)
NCC Number of Cargo Containers
TNS Total Number of Spaces (a.k.a. TNS = M x N)
NM Number of Moves
NR Number of Removes
M The number of Rows (a.k.a. MNCPS)
N The number of Columns (a.k.a. NS)

## Slide 33: Extra Slides
Additional Slides

## Slide 34: Pre-Marshalling Algorithm
Pre-Marshalling (Reshuffling)
(Examples)

## Slide 35: HW Set #1 – Problem 6 Special Team’s Project
Referring to the instructor’s (26 page) notes on “Port Container Terminals”, and based on the explanation/discussion and illustrated example shown on page 17-26 (Pre-marshalling, or Reshuffling algorithm):
  Write a “General” step-by-step computer program (any computer language) for the reshuffling operations.
  Solve for the initial storage layout:
    NS = 4
    MNCPS = b_max = 3
    NS > MNCPS
  Solve for the initial storage layout:
    NS = 4
    MNCPS = b_max = 3
    NS > MNCPS
  NS = Number of Stacks
  MNCPS = Maximum Number of Containers Per Stack

## Slide 36: HW Set #1 – Problem 6 (h) - Solution
Solve for the initial storage layout:
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
Iteration # 1
  Moved Container 6 to Stack 2
Iteration # 2
  Moved Container 3 to Stack 2

## Slide 37: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 3
  Moved Container 8 to Stack 4
Iteration # 4
  Moved Container 4 to Stack 4
Iteration # 5
  Removed Container 1
Iteration # 6
  Removed Container 2

## Slide 38: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 7
  Removed Container 3
Iteration # 8
  Removed Container 4
Iteration # 9
  Removed Container 5
Iteration # 10
  Removed Container 6

## Slide 39: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 11
  Removed Container 7
Iteration # 12
  Removed Container 8

## Slide 40: HW Set #1 – Problem 6 (h) - Solution
Solve for the initial storage layout:
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
Iteration # 1
  Moved Container 4 to Stack 2
Iteration # 2
  Moved Container 8 to Stack 3

## Slide 41: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 3
  Moved Container 1 to Stack 2
Iteration # 4
  Moved Container 8 to Stack 1
Iteration # 5
  Moved Container 1 to Stack 1
Iteration # 6
  Moved Container 9 to Stack 1

## Slide 42: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 7
  Moved Container 6 to Stack 2
Iteration # 8
  Moved Container 3 to Stack 3
Iteration # 9
  Moved Container 9 to Stack 4
Iteration # 10
  Moved Container 6 to Stack 4

## Slide 43: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 11
  Moved Container 3 to Stack 4
Iteration # 12
  Removed Container 1
Iteration # 13
  Removed Container 2
Iteration # 14
  Removed Container 3

## Slide 44: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 15
  Removed Container 4
Iteration # 16
  Removed Container 5
Iteration # 17
  Removed Container 6
Iteration # 18
  Removed Container 7

## Slide 45: HW Set #1 – Problem 6 (h) - Solution
  * = Denotes empty space
Iteration # 19
  Removed Container 8
Iteration # 20
  Removed Container 9

## Slide 46: Results
Solve for the initial storage layout
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
Solve for the initial storage layout
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
Results:
  Number of Moves: 4
  Number of Removes: 8
  Remove [Order]: 1, 2, 3, 4, 5, 6, 7, 8
  Start Time: 2015.04.18.17.022.14
  End Time: 2015.04.18.17.022.14
Results:
  Number of Moves: 11
  Number of Removes: 9
  Remove [Order]: 1, 2, 3, 4, 5, 6, 7, 8, 9
  Start Time: 2015.04.18.17.023.12
  End Time: 2015.04.18.17.023.12

## Slide 47: Unloading Algorithm
Unloading
(Examples)

## Slide 48: HW Set #1 – Problem 5 Special Team’s Project
Referring to the instructor’s (26 page) notes on “Port Container Terminals”, and based on the explanation/discussion and illustrated example shown on page 13 (see Figure 11: Unloading Operations, and based on your results in Problem 4a,b,c):
  Write a “General” step-by-step computer program (any computer language) for the unloading operations.
  Solve for the initial storage layout
    NS = 4
    MNCPS = b_max = 3
    NS > MNCPS
  Solve for the initial storage layout
    NS = 3
    MNCPS = b_max = 4
    NS < MNCPS
  NS = Number of Stacks
  MNCPS = Maximum Number of Containers Per Stack

## Slide 49: HW Set #1 – Problem 6 (e) - Solution
Iteration # 1
  GOAL: Remove Container 1
  Moved Container 8 to Stack 4
Iteration # 2
  Removed Container 1
Solve for the initial storage layout
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
  * = Denotes empty space

## Slide 50: HW Set #1 – Problem 6 (e) - Solution
  * = Denotes empty space
Iteration # 3
  Removed Container 2
Iteration # 4
  GOAL: Remove Container 3
  Moved Container 4 to Stack 1
Iteration # 5
  Removed Container 3
Iteration # 6
  Removed Container 4

## Slide 51: HW Set #1 – Problem 6 (e) - Solution
  * = Denotes empty space
Iteration # 7
  GOAL: Remove Container 5
  Moved Container 7 to Stack 1
Iteration # 8
  Removed Container 5
Iteration # 9
  GOAL: Remove Container 6
  Moved Container 8 to Stack 2
Iteration # 10
  Removed Container 6

## Slide 52: HW Set #1 – Problem 6 (e) - Solution
  * = Denotes empty space
Iteration # 11
  Removed Container 7
Iteration # 12
  Removed Container 8

## Slide 53: HW Set #1 – Problem 6 (f) - Solution
Solve for the initial storage layout
  NS = 3
  MNCPS = b_max = 4
  NS < MNCPS
Iteration # 1
  GOAL: Remove Container 1
  Moved Container 6 to Stack 4
Iteration # 2
  Removed Container 1
  * = Denotes empty space

## Slide 54: HW Set #1 – Problem 6 (f) - Solution
Iteration # 3
  Removed Container 2
Iteration # 4
  GOAL: Remove Container 3
  Moved Container 6 to Stack 1
Iteration # 5
  GOAL: Remove Container 3
  Moved Container 4 to Stack 2
Iteration # 6
  Removed Container 3

## Slide 55: HW Set #1 – Problem 6 (f) - Solution
Iteration # 7
  Removed Container 4
Iteration # 8
  GOAL: Remove Container 5
  Moved Container 7 to Stack 3
Iteration # 9
  Removed Container 5
Iteration # 10
  Removed Container 6

## Slide 56: HW Set #1 – Problem 6 (f) - Solution
Iteration # 11
  Removed Container 7

## Slide 57: Results
Solve for the initial storage layout
  NS = 4
  MNCPS = b_max = 3
  NS > MNCPS
Solve for the initial storage layout
  NS = 3
  MNCPS = b_max = 4
  NS < MNCPS
Results:
  Number of Moves: 4
  Number of Removes: 8
  Remove [Order]: 1, 2, 3, 4, 5, 6, 7, 8
  Start Time: 2015.04.18.15.022.43
  End Time: 2015.04.18.15.022.43
Results:
  Number of Moves: 4
  Number of Removes: 7
  Remove [Order]: 1, 2, 3, 4, 5, 6, 7
  Start Time: 2015.04.18.15.027.13
  End Time: 2015.04.18.15.027.13